## Slide 1: Reducing Heliostat Field Costs
by Direct Measurement of the Mirror Orientation

## Slide 2
© www.Sun2Point.com
G.Rosinga (Sun2Point)
E. Du Marchie van Voorthuysen (SOLAQ B.V.)
P. C. van den Donker (Sun2Point)
Introduction
(MSc) Delft University (Electronics)
Factory automation & product design - Philips Electronics
Quality management - Bosch Security Systems
(Yearly production > 1,000,000 pcs.)

## Slide 3
Reducing Heliostat Field Costs
by Mass Manufacturing
© www.Sun2Point.com
Presentation for SolarPACES 2015 Conference
October 13-16, Cape Town, South Africa
Thursday 15/10/15 , 16:35, Room 2.60, Sun2Point

## Slide 4
© www.Sun2Point.com
Huge Heliostats ?

## Slide 5
© www.Sun2Point.com
or Small Heliostats ?

## Slide 6
Critical size boundaries:
Weight: related to manual installation
Inner sea container dimensions 2.35 x 2.39m
Lifting equipment and/or a factory on the terrain adds to the costs
Heliostat Sizes in Projects
© www.Sun2Point.com
Initial sizes (m2) | Successor sizes (m2)
120 | 140
15.6 | 20
1.1 | 2.2

## Slide 7
Sunshot Program Targets
© www.Sun2Point.com
The LCOE for the solar field has to decrease
9 cnts / kWh (2010) 2 cnts / kWh.

## Slide 8
© www.Sun2Point.com
Mass manufacturing small heliostats off site
vs Manufacturing large heliostats on site
Possible Solution (or Revolution?)
Two men can place small heliostats by hand
Mass manufacturing leads to efficiency and lower prices.
Fast learning by high quantities leads to increased reliability

## Slide 9
Small Quantities vs Mass Manufacturing
120 m2
8,000 heliostats
1:54
2.25 m2
432,000 heliostats

## Slide 10
Present Practice (1)
120 m2 Heliostats
Mirror modules are mounted on a frame in a temporary assembly plant
8 men involved during placement
Heavy lifting equipment required
© www.Sun2Point.com

## Slide 11
Present Practice (2)
15.6 m2 Heliostats
5 men involved during placement
Some heavy lifting equipment required
© www.Sun2Point.com

## Slide 12
Present Practice (3)
1.1 m2 Heliostats
© www.Sun2Point.com

## Slide 13
© www.Sun2Point.com
Mass Manufacturing Off Site
Two men can place small heliostats by hand
Mass manufacturing leads to efficiency and lower prices.
Fast learning with high quantities leads to increased reliability

## Slide 14
Major Mass Heliostat Properties
Can be hand carried for installation
    < 40 kg.
No cabling required
Remotely controlled by wireless communication
Self powered by solar cells.
Autonomous
Has buit-in ‘intelligence’
Requires minimal communication with the control centre
Simple foundation and fixation
  Compensates orientation changes or deviations of the support
Factory calibrated
Start up by providing the GPS information (time and location)
and the target direction.
© www.Sun2Point.com

## Slide 15
Locating the sun
The developed control box measures orientation towards earth,
independent of sagging, bending or torsion
No adjustment required
Direct Mirror Measurement
Locating the horizon
© www.Sun2Point.com

## Slide 16
Acceleration measurement related error
Optical measurement related error
© www.Sun2Point.com
Prototype Accuracy
Deviation (mRad)
-0.15
0.15
-0.10
0.10
0.00
Deviation (mRad)
0.00
-0.05
0.05
-0.10
0.10
-0.15
0.15

## Slide 17
© www.Sun2Point.com
Prototype Size

## Slide 18
Orientation Error Budget
Error budget
Steady windload component
Ground settling
The control box
Measurement error
Drive error
Support error
© www.Sun2Point.com
Notes: A measuemernt idea came to our mind:
What if we can measure directly towards the earth
That would circumvent a number of error sources.
Coudl this be realized ?
Based on the gravity acceleration and optical observation of the sun ?
The answer was “yes we can!”

## Slide 19
Automatic Foundation Placement
200,000
of these foundation
screw-poles
can be placed
in 10 months
© www.Sun2Point.com

## Slide 20
Reduced On Site Work
Breaks down the barriers on the path to small heliostats
© www.Sun2Point.com
Calibration work
Ground work
Cabling work
Factory calibrated measurement and control box
Wireless control
Solar cell powered

## Slide 21
Calibration 0.5
Installation 12.6
Wiring 0.5
Support 35.2
Mirror module
30
Drives 23.4
Electronics 3.9
Overhead/Other
22.1
60 m2 - 128 euro
Installation 10
Wiring 4
Support 13.5
Mirror module
30
Drives 14
Electronics 11
Overhead/Other
16
2.25 m2 - 98 euro
© www.Sun2Point.com
Costs / m2
No calibration !

## Slide 22
Costs of Electronics
Keyboard
Display
Microphone
Loudspeaker
Buzzer
© www.Sun2Point.com
The control box

## Slide 23
© www.Sun2Point.com
Low Priced Gears
No ‘Rocket Science’
Can be manufactured cheap

## Slide 24: Conclusions
Mass manufacturing will greatly reduce the costs of the heliostats
Additional measures will make the use of mass manufactured heliostats possible
Key to the above is our new DIRECT measurement method / Control box
Sun2Point has expertise in electronics and mass manufacturing
© www.Sun2Point.com